## Slide 1: 路由协议
路由协议 用于路由器选择路径和管理路由表
路由器路由的方式
一旦选择了一条路径后，路由器将路由被路由协议
它是数据包的运输工具
Network Protocol
Destination Network
Connected RIP IGRP
10.120.2.0 172.16.1.0 172.17.3.0
Exit Interface
E0 S0 S1
被路由协议: IP，IPX……
路由协议: RIP, IGRP……
172.17.3.0
172.16.1.0
10.120.2.0
E0
S0
Notes: Purpose: This figure introduces students to routing protocols and compares routing protocols to routed protocols.
Emphasize: If network 10.120.2.0 wants to know about network 172.16.2.0, it must learn it from its S0 (or possibly S1) interface.
Note: The two routing protocols that will be taught in this course are RIP and IGRP. They are both distance vector routing protocols.

## Slide 2
在TCP/IP协议栈中，Routed Protocol（IP）工作在网络层，而Routing Protocol工作在传输层或者应用层，他们之间的关系为：Routing Protocol 负责学习最佳路径，而Routed Protocol根据最佳路径将来自上层的信息封装在IP包里传输
路由协议和被路由协议的区别

## Slide 3: 路由器是如何进行选路？
路由器转发数据包的关键是路由表。
每个路由器中都保存着一张路由表，表中每条路由项都指明数据包到某子网或某主机应通过路由器的哪个物理端口发送，然后就可到达该路径的下一个路由器，或者不再经过别的路由器而传送到直接相连的网络中的目的主机。

## Slide 4: 什么是路由
要实现路由路由器必须知道:
  目的地址
  源地址
  所有可能的路由路径
  最佳路由路径
  管理路由信息
172.16.1.0
10.120.2.0
Notes: Purpose: This figure introduces students to routing. The router must accomplish the items listed in the figure for routing to occur.
Emphasize:
Path determination occurs at Layer 3, the network layer. The path determination function enables a router to evaluate the available paths to a destination and to establish the best path.
Routing services use network topology information when evaluating network paths. This information can be configured by the network administrator (static routes) or collected through dynamic processes (routing protocols) running in the network.
Transition:
How do you represent the path to the packet’s destination?

## Slide 5: 管理距离 Administrative Distances
管理距离主要用于不同路由协议之间的可信度。
可信度的范围是：0 到255 之间,它表示一条路由选择信息源的可信性值.该值越小,可信度越高.0 为最信任,255 为最不信任即没有从这条线路将没有任何流量通过.

## Slide 6: 路由的不可信度
IGRP Administrative
Distance=100
Router D
Router B
Router A
Router C
RIP Administrative
Distance=120
E
I need to send a packet to Network E. Both router B and C will get it there. Which route is best?
Notes: 5
Purpose: This figure introduces administrative distance.
Emphasize:
An administrative distance is a rating of the trustworthiness of a routing information source, such as an individual router or a group of routers. In a large network, some routing protocols and some routers can be more reliable than others as sources of routing information.
The default administrative distance for static routes and various routing protocols is listed in the student guide. The lower the distance, the more trustworthy the route is. For example, in the figure, the packet would learn the route learned via IGRP.

## Slide 7: 一些常用路由协议默认的AD值
直接相连:0
静态路由:1
EIGRP:90
OSPF:110
RIP:120

## Slide 8: 静态路由和动态路由
静态路由
  由网络管理员在路由器上手工添加路由信息以实现路由目的
动态路由
  根据网络结构或流量的变化，路由协议会自动调整路由信息以实现路由
Notes: Purpose: This figure introduces students to static and dynamic routes.
Emphasize:
Static knowledge is administered manually—A network administrator enters it into the router’s configuration. The administrator must manually update this static route entry whenever an internetwork topology change requires an update. Static knowledge can be private—by default it is not conveyed to other routers as part of an update process. You can, however, configure the router to share this knowledge.
Dynamic knowledge works differently. After the network administrator enters configuration commands to start dynamic routing, route knowledge is updated automatically by a routing process. Whenever new topology information is received from the internetwork, routers update neighbors about the route change.

## Slide 9: 静态路由
172.16.2.1
SO
172.16.1.0
B
172.16.2.2
Network
A
  在小型网络中适合设置静态路由。
B
Stub Network
Notes: Purpose: This figure describes how a static route operates.
Emphasize: For intercommunication, static routes must be configured in both directions. Static routes are often used to route traffic to a stub network or other network where only a single route to that network exists.

## Slide 10: 静态路由优缺点
优点：
1.对路由器CPU没有管理性开销
2.在路由器间没有带宽占用
3.增加安全性
缺点：
1.必须真正了解网络
2.对于新添网络配置繁琐
3.对于大型网络工作量巨大

## Slide 11: 静态路由的应用场合
一个小型到中型的网络，而且没有或只有较小的扩充计划时。
静态路由要手工输入，手工管理；管理开销对于动态路由来说是一个大大的负担。

## Slide 12: 静态路由的配置
  指定一条可以到达目标网络的路径
Router(config)#ip route network [mask] {address | interface}[distance] [permanent]
Notes: Purpose: This figure describes the command syntax used to establish an IP static route.
Emphasize: A static route allows manual configuration of the routing table. No dynamic changes to this table entry will occur as long as the path is active. Routing updates are not sent on a link that is only defined by a static route; hence, conserving bandwidth.
Describe the The ip route field descriptions:
    network—destination network or subnet
    mask—subnet mask
    address—IP address of next hop router
    interface—name of interface to use to get to destination network.
Transition: The next figure provides a static route configuration example.

## Slide 13: 静态路由的例子
Stub Network
ip route 172.16.1.0 255.255.255.0 172.16.2.1
172.16.2.1
SO
172.16.1.0
B
172.16.2.2
Network
A
B
  这是一条单方向的路径，必须配置一条相反的路径。
Notes: Purpose: This figure gives an example of a static route configuration.

## Slide 14: 静态路由的例子
2501(config)#ip route 172.16.1.0 255.255.255.0 172.16.2.1
172.16.1.0：目的网络
255.255.255.0：子网掩码
172.16.2.1：下一跳的IP地址
（也称为网关，离本子网最近的路由器接口地址）

## Slide 15: 静态路由的删除
静态路由的删除：
2501(config)#no ip route 172.16.1.0 255.255.255.0 172.16.2.1
2501(config)#

## Slide 16: 缺省静态路由
缺省路由就是在没有找到任何匹配的路由项情况下，才使用的路由。即只有当无任何合适的路由时，缺省路由才被使用。
在路由表中，缺省路由以到网络0.0.0.0（掩码为0.0.0.0）的路由形式出现。
缺省路由，用于INTERNET连接，安全性不好
2501(config)#ip route 0.0.0.0 0.0.0.0 s0

## Slide 17: 缺省路由
Stub Network
ip route 0.0.0.0 0.0.0.0 172.16.2.2
172.16.2.1
SO
172.16.1.0
B
172.16.2.2
Network
A
B
  使用缺省路由后，Stub Network可以到达路由器A以外的网络。
  在Stub Router（连接Stub Network的路由器）上通常配置缺省路由这也是大多数企业在接入INTERNET时所采用的配置
Notes: Purpose: This figure gives an example of a default route configuration.
Emphasize: With an address and subnet mask of 0.0.0.0 0.0.0.0 in the ip route statement, packets for any network not listed in the routing table will be sent to the next hop, 172.16.2.2.

## Slide 18: 缺省路由注意
在使用了缺省路由时，需要添加ip classless命令
原因：所有cisco路由器是有类的，即在接口默认 使用了默认的mask。当路由器收到一个目的子网不在路由表中的数据包时，默认，丢弃该数据包。因此在使用缺省路由时必须使用ip classless命令，因为在路由表中不会包含远端子网信息