## Slide 1: 动态路由协议
距离向量(distance vector)主要有：RIP IGRP
链路状态(link state)有OSPF IS-IS
混合型(hybrid)有EIGRP

## Slide 2: 距离矢量的路由协议
定期将路由表复制给相邻的路由器并且进行矢量堆加
C
D
B
A
C
B
A
D
Routing
Table
Routing
Table
Routing
Table
Routing
Table
Distance—How far Vector—In which direction
Notes: Purpose: This figure introduces the distance vector routing algorithm, the first of the classes of routing protocols, and outlines how it operates.
Emphasize: Distance vector algorithms do not allow a router to know the exact topology of an internetwork.
This information is somewhat analogous to the information found on signs at a highway intersection. A sign points toward a road leading away from the intersection and indicates the distance to the destination.
Further down the highway, another sign also points toward the destination, but now the distance to the destination is shorter.
So long as each successive point on the path shows that the distance to the destination is successively shorter, the traffic is following the best path.

## Slide 3: DV路由协议的特征
采用周期性的完全更新(发送整个路由表)和触发更新结合的路由更新方式
采用广播的方式进行路由更新（RIPv2采用的是组播）
DV的路由协议有RIPv1，RIPv2，IGRP
EIGRP和BGP属于高级的DV协议，他们学习路径的方式更多的趋近于DV，但是他们具备很多LS的特征（比如触发更新，组播更新等）

## Slide 4: 距离矢量—源信息的获得
路由器从收集到的源信息中选择到达目标地址的最佳路径
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
Routing Table
10.2.0.0
10.3.0.0
0
0
S0
S1
Routing Table
10.3.0.0
S0
0
10.4.0.0
E0
0
Routing Table
10.1.0.0
10.2.0.0
E0
S0
0
0
Notes: Layer 1 of 3:
Purpose: This figure continues the concept of how a router using a distance vector protocol generally discovers the best path to destinations from each router neighbor.
Emphasize: Layer 1 shows the topology consisting of four networks and three routers. Routing tables inside each router begin with entries for the 0 distance to directly connected networks.

## Slide 5: 距离矢量—源信息的获得
路由器从收集到的源信息中选择到达目标地址的最佳路径
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
Routing Table
10.1.0.0
10.2.0.0
10.3.0.0
Routing Table
10.2.0.0
10.3.0.0
10.4.0.0
10.1.0.0
0
0
1
1
S0
S1
S1
S0
Routing Table
10.3.0.0
S0
0
10.4.0.0
E0
0
10.2.0.0
S0
1
E0
S0
S0
1
0
0
Notes: Layer 1 of 3:
Emphasize: Layer 2 adds routing entries received some time later about noncontiguous networks that have distances of 1 from the given routers.

## Slide 6: 距离矢量—源信息的获得
路由器从收集到的源信息中选择到达目标地址的最佳路径
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
Routing Table
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
Routing Table
10.2.0.0
10.3.0.0
10.4.0.0
10.1.0.0
0
0
1
1
S0
S1
S1
S0
Routing Table
10.3.0.0
S0
0
10.4.0.0
E0
0
10.2.0.0
S0
10.1.0.0
S0
1
2
E0
S0
S0
S0
1
2
0
0
Notes: Layer 1 of 3:
Emphasize: Layer 3 adds the final entries received some time later that have distances of 2 from routers A and C.

## Slide 7: 距离矢量—管理路由信息
路由表的更新过程将通过路由器之间一步一步来完成
A
更新路由表
网络结构的
改变将导致
路由表的
更新
Notes: Layer 1 of 3:
Purpose: This figure continues the concept of how a router using a distance vector protocol generally performs its routing information update process when the network topology changes.
Emphasize: This layer shows the bullet point, the router on the right, and, on the right, a topology change; routing tables will need updating to reflect this topology change.

## Slide 8: 距离矢量—管理路由信息
路由表的更新过程将通过路由器之间一步一步来完成
A
更新路由表
在下一个周期后
路由器A发送更新
过的路由表
网络结构的
改变将导致
路由表的
更新
Notes: Layer 2 of 3:
Emphasize: Layer 2 adds the updated routing table that router A sends out after it processes the topology change.

## Slide 9: 距离矢量—管理路由信息
路由表的更新过程将通过路由器之间一步一步来完成
A
B
更新路由表
更新路由表
网络结构的
改变将导致
路由表的
更新
在下一个周期后
路由器A发送更新
过的路由表
Notes: Layer 3 of 3:
Layer 3 adds router B, which receives the updated routing table from router A. In turn, router B will perform its own process to update its routing table given this new topology update from router A.
Distance vector updates occur step by step.
Typically, a router sends updates by multicasting its table on each configured port, but other methods, such as sending the table only to preconfigured neighbors, are employed by some routing algorithms.
Multicast is used by the RIP2, OSPF, and EIGRP routing protocols. RIP and IGRP use broadcast.
The routing table can be sent routinely and periodically, or whenever a change in the topology is discovered. Updates sent when changes occur are called triggered updates.

## Slide 10: 收敛时间
收敛时间 （convergence time):从网络拓扑发生变化到网络中所有路由器都知道这个表化的时间就叫 收敛时间

## Slide 11: 路 由 回 环
每一个节点管理着与之相连的所有网络
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
Routing Table
10.3.0.0
S0
E0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
0
Routing Table
10.1.0.0
E0
S0
S0
S0
1
2
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
10.2.0.0
S0
S1
S1
S0
1
1
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Slide 1 of 4:
Prupose: This figure describes the first of the general problems that a distance vector protocol could face without the corrective influence of some countermeasure.
Emphasize: Layer 1 shows the original state of the network and routing tables. All routers have consistent knowledge and correct routing tables. In this example, the cost function is hop count so the cost of each link is 1. Router C is directly connected to network 10.4.0.0 with a distance of 0. Router A’s path to network 10.4.0.0 is through router B, with a hop count of 2.

## Slide 12: 路 由 回 环
缓慢的收敛容易造成路由信息的不一致
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
E0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
Down
Routing Table
10.1.0.0
E0
S0
S0
S0
1
2
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
10.2.0.0
S0
S1
S1
S0
1
1
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Slide 2 of 4:
Emphasize: In Layer 2, router C has detected the failure of network 10.4.0.0 and stops routing packets out its E0 interface. However, router A has not yet received notification of the failure and still believes it can access network 10.4.0.0 through router B. Router A’s routing table still reflects a path to network 10.4.0.0 with a distance of 2.

## Slide 13: 路 由 回 环
路由器C 推断到达10.4.0.0 网络的最好路径是通过路由器B
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
2
Routing Table
10.1.0.0
E0
S0
S0
S0
1
2
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
10.2.0.0
S0
S1
S1
S1
1
1
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Slide 3 of 4:
Emphasize: Because router B’s routing table indicates a path to network 10.4.0.0, router C believes it now has a viable path to 10.4.0.0 through router B. Router C updates its routing table to reflect a path to network 10.4.0.0 with a hop count of 2.

## Slide 14: 路 由 回 环
路由器 A 根据错误的信息升级它的路由表
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
S0
S0
S0
S0
1
2
10.3.0.0
10.1.0.0
10.2.0.0
10.4.0.0
0
2
Routing Table
E0
S0
S0
S0
1
4
10.1.0.0
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
S0
S1
S1
S0
3
1
10.2.0.0
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Slide 4 of 4:
Emphasize: In Layer 4, router A receives the new routing table from router B, detects the modified distance vector to network 10.4.0.0, and recalculates its own distance vector to network 10.4.0.0 as 3.
If all routers in an internetwork do not have up-to-date, accurate information about the state of the internetwork, they might use incorrect routing information to make a routing decision.
The use of incorrect information might cause packets to take less-than-optimum paths or paths that return packets to routers that they have already visited.

## Slide 15: 无 限 计 数
10.4.0.0 网络的跳数将无限大
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
4
Routing Table
E0
S0
S0
S0
1
6
10.1.0.0
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
S0
S1
S1
S0
5
1
10.2.0.0
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Purpose: This figure describes another of the general problems that a distance vector protocol could face without the corrective influence of some countermeasure.
Emphasize: Both routers conclude that the best path to network 10.4.0.0 is through each other and continue to bounce packets destined for network 10.4.0.0 between each other, incrementing the distance vector by 1 each time.
This condition, called count-to-infinity, continuously loops packets around the network, despite the fundamental fact that the destination network 10.4.0.0 is down. While the routers are counting to infinity, the invalid information allows a routing loop to exist.
A related concept is the Time-to-Live (TTL) parameter. The TTL is a packet parameter that decreases each time a router processes the packet. When the TTL reaches zero, a router discards or drops the packet without forwarding it. A packet caught in a routing loop is removed from the internetwork when its TTL expires.

## Slide 16: Routing Loops（路由环路）
Packets for network 10.4.0.0 bounce (loop) between routers B and C.
Notes: Slide 4 of 4
Emphasize: In Layer 4, router A receives the new routing table from router B, detects the modified distance vector to network 10.4.0.0, and recalculates its own distance vector to network 10.4.0.0 as 3.
If all routers in an internetwork do not have up-to-date, accurate information about the state of the internetwork, they might use incorrect routing information to make a routing decision.
The use of incorrect information might cause packets to take less-than-optimum paths or paths that return packets to routers that they have already visited.

## Slide 17: DV中解决环路的几种办法
水平分割
毒性逆转
保持失效定时器
触发更新
最大跳数（终极武器）

## Slide 18: Split Horizon（水平分割）
不会接收到由自身传达出去的路由信息
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
X
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
0
Routing Table
E0
S0
S0
S0
1
2
10.1.0.0
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
S0
S1
S1
E1
1
2
10.2.0.0
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Purpose: This figure introduces the corrective measure known as “split horizon.” The split horizon technique attempts to solve routing loops.
Emphaisze: The split horizon technique attempts to eliminate routing loops and speed up convergence. The rule of split horizon is that it is never useful to send information about a route back in the direction from which the original packet came. In the example:
  Router C originally announced a route to network 10.4.0.0 to router B. It makes no sense for router B to announce to router C that router B has access to network 10.4.0.0 through router C.
  Given that router B passed the announcement of its route to network 10.4.0.0 to router A, it makes no sense for router A to announce its distance from network 10.4.0.0 to router B.
  Because router B has no alternative path to network 10.4.0.0, router B concludes that network 10.4.0.0 is inaccessible.
In its basic form, the split horizon technique simply omits from the message any information about destinations routed on the link. This strategy relies either on routes never being announced or on old announcements fading away through a timeout mechanism.
Split horizon also improves performance by eliminating unnecessary routing updates. Under normal circumstances, sending routing information back to the source of the information is unnecessary.

## Slide 19: Route Poisoning（路由中毒）
路由器将该路由信息的跳数标记为无限大
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
Infinity
Routing Table
10.1.0.0
E0
S0
S0
S0
1
2
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
10.2.0.0
S0
S1
S1
E1
1
2
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Purpose: This figure expands on the split horizon technique by adding the concept of poisonous reverse updates.
Emphasize: Route poisoning closes the potential for longer routing loops. Fast convergence minimizes the chance for a routing loop to occur, but even the smallest interval leaves the possibility open. With a poison route in place, router B can maintain a steadfast entry that network 10.4.0.0 is indeed down.

## Slide 20: Poison Reverse（毒性逆转）
反转毒杀可以超越水平分割
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
Infinity
Routing Table
10.1.0.0
E0
S0
S0
S0
1
2
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
10.2.0.0
S0
S1
S1
E1
Possibly Down
2
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Poison Reverse
Notes: Purpose: This figure explains poison reverse..
Emphasize: Poison reverse overrides the split horizon solution.

## Slide 21: Holddown Timers （保持失效定时器）
路由器在Hold-Down时间内将该条记录标记为possibly down以使其它路由器能够重新计算网络结构的变化
Network 10.4.0.0 is down
then back up
then back down
Update after
hold-down Time
Network 10.4.0.0
is unreachable
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Update after
hold-down Time
Notes: Purpose: This figure describes how hold-down timers avoid the general problems that a routing protocol could face.
Emphasize: Hold-down timers are used to prevent regular update messages from inappropriately reinstating a route that may have gone bad.
Hold-downs tell routers to hold any changes that might affect routes for some period of time.
The hold-down period is usually calculated to be just greater than the period of time necessary to update the entire network with a routing change.
Note: A network administrator can configure the hold-down timers on several routers to work together in tandem.

## Slide 22: Triggered Updates（触发更新）
当路由表发生变化时路由器立即发送更新信息
A
B
C
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Network 10.4.0.0
is unreachable
Network 10.4.0.0
is unreachable
Network 10.4.0.0
is unreachable
10.1.0.0
Notes: Purpose: This figure describes how triggered updates avoid the general problems that a routing protocol could face.
Emphasize: Normally, new routing tables are sent to neighboring routers on a regular basis. A triggered update is a new routing table that is sent immediately, in response to some change.
Each update triggers a routing table change in the adjacent routers, which, in turn, generate triggered updates notifying their adjacent neighbors of the change. This wave propagates throughout that portion of the network where routes went through the link.
Triggered updates would be sufficent if we could guarantee that the wave of updates reached every appropriate router immediately. However, there are two problems:
  Packets containing the update message can be dropped or corrupted by some link in the network.
  The triggered updates do not happen instantaneously. It is possible that a router that has not yet received the triggered update will issue a regular update at just the wrong time, causing the bad route to be reinserted in a neighbor that had already received the triggered update.
Coupling triggered updates with holddowns is designed to get around these problems. Because the hold-down rule says that when a route is removed, no new route will be accepted for the same destination for some period of time, the triggered update has time to propagate throughout the network.

## Slide 23: Max-Hop（最大跳数）
指定最大跳数来防止路由回环
A
B
C
10.1.0.0
10.2.0.0
10.3.0.0
10.4.0.0
E0
S0
S0
S1
S0
E0
X
Routing Table
10.3.0.0
S0
S0
S0
S0
1
2
10.1.0.0
10.2.0.0
10.4.0.0
0
16
Routing Table
E0
S0
S0
S0
1
16
10.1.0.0
10.4.0.0
10.3.0.0
10.2.0.0
0
0
Routing Table
S0
S1
S1
S0
16
1
10.2.0.0
10.1.0.0
10.4.0.0
10.3.0.0
0
0
Notes: Purpose: This figure describes a corrective measure that attempts to solve the routing loop problems that a distance vector protocol could face.
Emphasize: Routing loops occur only when routing knowledge being propagated has not yet reached the entire internetwork—when the internetwork has not converged after a change. Fast convergence minimizes the chance for a routing loop to occur, but even the smallest interval leaves the possibility open.
To avoid prolonging the count-to-infinity time span, distance vector protocols define infinity as some maximum number. This number refers to a routing metric, such as a hop count.
With this approach, the routing protocol permits the routing loop until the metric exceeds its maximum allowed value. This example shows this defined maximum as 16 hops. Once the metric value exceeds the maximum, network 10.4.0.0 is considered unreachable.

## Slide 24: RIP
在IGP中，RIP是个广泛使用的协议
RIP也称距离矢量协议，用信息包所经过的网关来做距离的单位，超过15跳便无法到达
IGRP是CISCO专用的路由协议，可以服务于大型互连网络，不受限于16跳的限制（默认是100跳）

## Slide 25: RIP 概 述
19.2 kbps
T1
T1
T1
  Hop 计算
  路由器每隔30秒更新
  最多支持相同hop数的6条路径，实现负载均衡
Notes: 5
Purpose: This figure presents general information about RIP.
Emphasize: The figure shows a network. The arrows highlight the path RIP selects. RIP selects the best path based on shortest hop count so it ignores the path with the faster T1 links.
Be sure that you do not disparage RIP. It was developed in a homogeneous network. If everything is connected via a single media type, then bandwidth-based metrics reduce to hop count. In some cases RIP is more appropriate than other protocols. It is extremely well tested.

## Slide 26: RIP概述
RIP是通过UDP端口520来进行操作的,RIP信息包是封装在UDP segment中的.RIP定义了2种信息类型
Request message(请求信息)和Response message(应答信息).请求信息是用来向邻居请求发送一个update(更新),应答信息运载着这个被请求的update.
RIP的 metric是基于hop count(跳数)的,metric为16代表不可达

## Slide 27: RIP概述
在刚启动的时候,RIP从启用了RIP的接口上向外广播请求信息,接下来RIP进程进入一个循环状态:监听来自其他路由器的请求信息和应答信息.当邻居收到请求信息以后,就发送应答信息给这个发出请求信息的路由器
在RIP启动之后,平均每30秒,启用了RIP的接口会发送应答信息(也就是update),这个update包含了路由器完整的路由表.